## Slide 1
Increasing Throughput in Disrupted Networks
Congestion Modeling Using Path Prediction
Ed Birrane
birrane1@umbc.edu
May 2nd, 2011

## Slide 2: Definition What is a Delay/Disruption-Tolerant Network?
Challenged Networks
  Little power/comm infrastructure
  Wireless data transmission
  Mobile Platforms
  Scalable Deployments
  Hostile Environments
Per-Link Failures
  Signal Propagation Delays
  Intermittent Transmission Disruption
  Data latency through the entire network
DTN is a subset of challenged networking dominated by delays in data processing incurred by link impairments and latencies.
We will focus on a motivating example: The Solar System Internet

## Slide 3: Core Enabling Functions How do they work?
Durable Storage of Data in Transit
  Store-and-forward operations where data survives interruptions in connectivity
Custody Transfer
  Incremental data advances through the network
    No requirement for end-to-end retransmission
Asserted Communications Parameters
  Pre-planned parameters, push-methods, and error recovery
    No requirement for discovery and negotiation in the network
Delegation
  Capture universal functions in a logical overlay
  Push heterogeneous function to supporting per-link layers.
Operator-in-the-loop management, pre-configuration, and small, dense population.

## Slide 4: Problème du Jour How do we Increase Throughput Through the Network?
Assumptions
  Semi-structured networks: Data has a general “direction” and node motion is somewhat regular
  Vast expanse: Dense node populations unfeasible
  Time Matters: Network topology constantly changing over time.
Problem Statement
  Given local topological information, construct efficient paths through the network that consider both changes in topology and traffic-based congestion.
Hi! I’m NP Complete from Steiner Tree in Graphs!
Information at one node

## Slide 5: Importance Why do we need to be efficient?
You never get a second chance to make a first connection.
Sensing nodes fill up.
You will miss a critical event or science observation if your recorders are full.
Retransmission is expensive.
We have very power-constrained systems.
You might need to wait days or weeks for connectivity.
You might need to renegotiate access (NASA -> ESA -> JAXA)
Path set-up is costly, so get it right.
Slewing spacecraft
Power transmitters/receivers
Negotiating Deep Space Network time.

## Slide 6: Prior Work How do we Route Data in Challenged Networks Now?
Space systems pre-configure everything.
  Capturing and downlinking observations takes weeks to months of preparation.
  Nothing is trusted for automation.
Mobile, Ad-Hoc Networks (MANets) flood.
  Node mobility is random (ad-hoc)
  Some heuristics for constrained multi-cast.
Contact-Graph Routing (CGR) is compromise.
  Construct a contact graph at each local node.
  Run your favorite graph algorithm to build a path.
  Allows for asserted information (space systems)
  Can be built over flooded information (MANets).
  Doesn’t save path information! Forwarding only!
DTN routing is governed either by operator-in-the-loop configuration or epidemic/probabilistic multicast.

## Slide 7: Bright Idea #1 Path Routing!
Don’t re-calculate path at every node.
  That’s computationally expensive
Propagate local node knowledge.
  Downstream nodes know about upstream knowledge.
  If they don’t match, can send backprop messages.
Make message travels deterministic.
  Especially useful for overlay networks using multiple data link layers.
  Absent, of course, error.
CGR calculates a full path, then discards it in lieu of constructing next-hop neighbors. Save the paths (dynamic programming)
Augment messages with their calculated path (virtual circuit) and relevant contacts.

## Slide 8: Bright Idea #2 Modify the Local Contact Graph with Capacity Information
Builds congestion model around two important localities of reference
  Spatial locality: Message types may follow common paths.
  Temporal locality: Sensor report times may cause periodic bursts.
CGR naturally considered contact’s estimated capacity (EC)
  Tweaking EC outside of the CGR algorithm causes the information to be auto-incorporated into the routing decision.
Gives a mechanism for backpressure
  If path validation fails, can pass EC information upstream to inform stakeholders in some common path.
If we know when a message will be where, we can remember how it affects the link capacity and avoid saturated links.

## Slide 9: Conclusion and Future Work
Routing in Challenged Networks
  DTNs (especially sensing networks) support a semi-structure that may be exploited to improve routing efficiency.
  Avoiding retransmission and congestion is important to getting the most data through the network at a given time.
Existing Methods Focus on Hand-Tuning or Near-Broadcast
  Very few automated methods exploit the semi-structure of these networks.
  CGR provides a foundation (when modified) to build path routing and congestion prediction.
Future Work
  Working with CGR authors to spin the RFC to include path routing.
  Working simulations to demonstrate throughput increase with these methods.
  Following research to demonstrate ability to construct contact graphs in a variety of networks.
Path routing with capacity modeling makes routing more efficient. Future work will demonstrate you can build contact graphs in less structured networks.

## Slide 10: Questions?
This isn’t Routing… It’s Forwarding with Style…
http://theipadkids.com/toy-story-read-along-love-it