Introduction:

The PAULMON debugger is my attempt to make a user-friendly 8051
debugger, with enough on-line information that it should be
unnecessary to read this doc file.  PAULMOM is targeted for
use by the microprocessor design course at Oregon State, but
may be used by anyone (who can figure it out) for projects
ranging from research to commercial products.  PAULMON is
free and may not be distributed for profit whatsoever.

Since I don't expect Prof's or TA's at OSU to make students
aware of this documentation nor to provide it nor do I 
expect students to read much of it, I wrote PAULMON to
be very simple and to provide lots of on-line clues about
what it can do and how to go about it.  I hope that you
find PAULMON to be useful and easy to use.  Good Luck.

                                 -Paul Stoffregen
                                   (paul@ece.orst.edu)

DISCLAIMER: This is free software.  As far as warranty is
concerned, you get exactly what you pay for!  I have
tried to make this code as good as possible during the
four weeks I worked on it, but nobody is perfect and
portions (the single step in particular) were never well
tested.  USE AT YOUR OWN RISK.  The assembly source is
provided in case there's something you don't like.

ADDITIONAL DISCLAIMER: This doc file has lots of tyopes
and other errorss, and I really don't care.  PAULMON
was written to be easy enough that this file ought to
be unnecessary, but people ask for it nonetheless,
usually before they even try to use the thing.

What You Will Need to use it:

PAULMON is 8051 assembly code which is intended to be
burned into a 2764 EPROM, though a pair of 2732's
could be used or a bigger rom can be used with the
rest being empty or filled with other code.  The
EPROM with PAULMON should be addressed so that it
is read from 0000 to 1FFF with the 8051's EA pin
wired to make it read all code from external memory.

PAULMON uses the built in UART in the 8051 to
communicate with the user.  Typically, a PC computer
is used with a terminal program, an 8051 assembler,
and a text editor to form a simple, low cost 8051
development system with PAULMON.  A serial line
receiver and driver should be used (the MAX232 is
a good choice, IMHO) to interface the 8051 to the
PC's serial port.  Only TxD, RxD and ground are
used (no handshaking) and PAULMON adapts to use
whatever baud rate the computer is using (if it
can with the crystal you select, see below)

PAULMON is intended to be used with RAM as well, and
the default location for the beginning of the RAM is
2000 (hex), right after the EPROM, though the RAM
can be used anywhere in the range of 2000 - FFFF.
The read enable signal to the RAM should be the
logical OR of the RD and PSEN signals, so that read
attempts to external code memory or program memory
spaces will read from the RAM.  (use an AND gate to
do the logical OR of these signals, since they
are active low!)  Obviously the write enable of the
RAM should be connected to the WR pin of the 8051.

Having a RAM connected in this way will allow the
download command in PAULMON to write your program
into the RAM (writing into the external data memory
space).  Then you can run your program, since
read attempts from the external program memory space
will read from the RAM chip.

How to get is set up:

Design and build your 8051 board.  All that is really
required is the 8051, an EPROM, a latch (74xx373),
some sort of address decoding to enable the EPROM
for memory access between 0000-1FFF, and a line 
receiver to convert the high voltage RS232 to a
TTL (or CMOS) compatible signal (or else you'll
toast the 8051 before it even has a chance).

To really use PAULMON, a RAM is required as well
as the AND gate to allow both program and data
read cycles to read the RAM memory, and a reset
button to easily get back to PAULMON when your
program crashes.

With just the minimal setup, set the computer's
baud rate to something slow (like 1200 bps) and
power up the board.  Press Enter (Return) and
hopefully you'll see a screenful of text from
PAULMON.  PAULMON does not send line feed
characters, so the terminal emulator software
must be configured to translate CR -> CR/LF.
(PAULMON ignores LF characters is receives.)
If the entire message ends up on one line, then
the terminal is not translating CR -> CR/LF.
After it works, you can try increasing the baud
rate and COLD-BOOTING (you must turn the power
off, taking the reset line high will not make
PAULMON look for the new baud rate... or change
the bytes where it stores the old baud rate...
see the code if you're interested)  If the 
minimal system shows no signs of life, it's
time to check the wiring, usually starting by
making sure you didn't swap the TxD and RxD
lines.

The Automatic Baud Rate detection:

This code was borrowed from MDP/51 by Kei-Yong Khoo.  It is run 
immediatly after a system reset.  It waits for a <RETURN> 
character, and uses it to calculate the timer #1 reload value.  
Some modifications have been made to Khoo's code.  It requires 
only one character.  It also stores the reload value in four 
memory locations in internal ram (78H, 79H, 7AH, and 7BH).  These 
four locations are unlikely to be changed during a user program's 
execution or while the debugger is running.  When another reset 
occurs (without removing the power) the program looks at those 
four locations.  If all four agree, then it uses that reload 
value and does not require another keypress.  It is interesting 
to note that occasionally, with cystal values which produce exact 
reload values (such an 7.3728 MHz), the baud rate detection 
routine may not correctly calculate the reload value.  Garbage 
will get printed all over the screen.  If this happens, just 
switch off the power and try again.  The advantage of crystals 
such as the 7.3728 Mhz is that they allow transmission at speeds 
of 9600 and 19200 baud!  It is highly reccomended that you use 
the highest possible baud rate with this debugger, as is tends to 
print quite a bit of text to the screen.

On-line Help:

By typing '?' at the main menu, a help screen summarizing the 
available commands is printed.  On-line help is also available 
regarding the single step run feature.  This help is accessed by 
typing '?' just after using the 'R' command.  While in the single 
step mode, a summary of commands is also available, again by 
typing '?'.

The <ESC> key:

The <ESC> key is supported extensively.  It will abort all 
commands from any prompt.  It will stop the list and hex dump 
commands in the middle of their printing.  It will also interrupt 
the printing of text to the screen!  This is useful at slow baud 
rates, since a full screen of text can take quite a while to 
print at 300 baud.  

The Download Program command (type 'D')

This allows you to send the object code from the assembler to the 
external ram.  The object file must be a standard Intel Hex 
Format file, such as the .OBJ file created by the Psuedo-
Assembler, by Psuedo-Corp.  The file must be sent as an ASCII 
transfer.  The protocal such as XMODEM is used.  Pressing the 
<ESC> key at any time will abort the transfer.  Please note that 
most communications programs use the <ESC> key to abort their 
transfer.  In this is the case, the first <ESC> will halt the 
terminal, pressing it again will abort the recieve at the 
8051/31. Unlike some other debuggers, PAULMON will recognize
the <ESC> key anywhere in the middle of the incoming data,
not just at the beginning of a line.

The Run Program command (type 'R')

The run command allows you to execute your program.  Two types of 
run are supported, Normal and Single-Step.  The single step mode 
is explained later, as it is fairly complex.  During a normal 
run, the quiviliant of an LCALL to your code is given.  During 
the execution of your program, the debugger obviously has no 
control of the system, unless of course your program calls one of 
the subroutines offered by the degugger in the jump table at 
location 0030H.  After specifying which run mode you need, the 
location of your program is prompted, with the current memory 
pointer value as the default choice.  As is the case at all 
prompts, pressing the <ESC> key will abort the run command.  It 
is interesting to note that the run command leaves timer #1 in 
auto-baud rate generation mode.  If serial communication is 
desired at the same baud rate as that used for the debugger, 
timer #1 need not be given a new reload value.  It is recommended 
that the character input and output routines from the debugger be 
used via the jump table.
                        
The New Memory Location command (type 'N')

The debugger operates with a pointer to the data memory with 
which you are working.  This pointer is used by the list and hex 
dump command.  It is also the default run location.  The pointer 
is incremented as memory is viewed or modified.  Just type 'N' to 
change it.

The List command (type 'L')

This debugger gives you the ability to list your program's code 
directly from the computer's memory.  All the 8051/31 mnemunonics 
are supports, as well as the names of the special function 
registers.  Bit addressable locations are displayed using the 
standard syntax (e.g. PWS.2 or 20.5), but individual bit location 
names are not supported (e.g. SCON.0 will print in place of RI).  
Obviously, the original labels used in the source code cannot be 
printed, instead the memory locations are displayed.  Other 
special Intel assembly formats, such as $ and CALL are not 
supported.  However, the list command can provide a reassuring 
look at the program directly from the memory.

The Hex Dump command (type 'H')

By typing 'H', the next 256 bytes of ram are dumped to the screen 
in hex and ascii.  The <ESC> key may be pressed to abort the 
printout.

The Edit command (type 'E')

This command allows you to change the values of memory locations 
in the external ram.  Each location's old value is shown.  If 
<ESC> is pressed, the current location's value is not changed.

The Jump Table:

Desipte the use of the word "jump", the user must LCALL to these 
locations!  The individual locations contain jumps to the 
subroutines, which all terminate with a RET.  The table provides 
the user with a memory location to call to that WILL NOT CHANGE 
if the debugger is reassembled.  The routines available are:

        0030:   Cout    -Sends the byte in Acc to the
                         serial port.
        0032:   Cin     -Waits for a character from
                         the serial port, returned in Acc.
        0034:   pHex    -Prints the two digit hex value 
                         in Acc to the serial port.
        0036:   pHex16  -Prints the four digit hex value
                         in DPTR to the serial port.
        0038:   pString -Prints the string in code memory
                         pointed to by DPTR to the serial
                         port.  The string must terminate
                         with 00H or a high bit set
        003A:   gHex    -Gets a two digit hex value from
                         the serial port, returned in Acc
        003C:   gHex16  -Gets a four digit hex value from
                         the serial port, returned in DPTR
        003E:   Esc     -Checks to see if the <ESC> key is
                         waiting in SBUF.  Clears the buffer
                         if it is, and returns with the
                         carry set.  Otherwise, leaves SBUF
                         untouched, and returns with C=0.
        0040:   Upper   -Converts character in Acc to
                         uppercase if it is lowercase.
        0042:   Init    -Automatic baud rate detection.

The memory location can be placed directly in your code, or an 
EQU can be used to make your code more readable.  For example:

Program:.EQU    gHex16, 003AH           ;this make the code nice
        MOV     DPTR, #StrLoc           ;load DPTR 
        LCALL   gHex16                  ;print the DPTR
        MOV     A,#13
        LCALL   0030H                   ;print a <RET>
        LCALL   0038H                   ;print the string
        RET
StrLoc: .DB     "This is my String.", 0

Most of these routines leave the registers unchanged, however, it 
is a good idea to consult the source code just to be sure...
In particular, the phex routine DESTROYS the contents of Acc, so
beware.  (this has cause some people some grief, who had assumed
the phex would leave Acc unchanged.  If you want it unchanged,
the original .ASM file is provided for you to modify)

The Single-Step Run:


[This part was never written, and the single step run code is
somewhat buggy, primarily due to a lack of available beta
testers... so docs were never written, but PAULMON ought to give
you enough clues to figure it out if you try.]