## Slide 1: Graphics Pipeline Rasterization
CMSC 435/634

## Slide 2: Drawing Terms
Primitive
  Basic shape, drawn directly
  Compare to building from simpler shapes
Rasterization or Scan Conversion
  Find pixels for a primitive
  Usually for algorithms that generate all pixels for one primitive at a time
  Compare to ray tracing: all primitives for one pixel

## Slide 3: Line Drawing
Given endpoints of line, which pixels to draw?

## Slide 4: Line Drawing
Given endpoints of line, which pixels to draw?

## Slide 5: Line Drawing
Given endpoints of line, which pixels to draw?
Assume one pixel per column (x index), which row (y index)?
Choose based on relation of line to midpoint between candidate pixels
?
?
?
?
?
?
?
?

## Slide 6: Line Drawing
Choose with decision variable
Plug midpoint into implicit line equation
Incremental update

## Slide 7: Line Drawing
Implicit line equation
Midpoint algorithm
  y = y0
  d = f(x0+1, y0+0.5)
  for x = x0 to x1
    draw(x,y)
    if (d < 0) then
      y = y+1
      d = d + (x1 - x0) + (y0 - y1)
    else
      d = d + (y0 - y1)

## Slide 8: Polygon Rasterization
Problem
  How to generate filled polygons (by determining which pixel positions are inside the polygon)
  Conversion from continuous to discrete domain
Concepts
  Spatial coherence
  Span coherence
  Edge coherence

## Slide 9: Scanning Rectangles
for ( y from y0 to y1 )
for ( x from x0 to x1 )
Write Pixel (x, y)

## Slide 10: Scanning Rectangles (2)
for ( y from y0 to y1 )
for ( x from x0 to x1 )
Write Pixel (x, y)

## Slide 11: Scanning Rectangles (3)
for ( y from y0 to y1 )
for ( x from x0 to x1 )
Write Pixel (x, y)

## Slide 12: Barycentric Coordinates
Use non-orthogonal coordinates to describe position relative to vertices
  Scaled edge equations
    0 on edge, 1 at opposite vertex

## Slide 13: Barycentric Example

## Slide 14: Barycentric Coordinates
Computing coordinates
  Equations for α, β and γ in book
  Solutions to linear equations of x,y
Ratio of areas / ratio of cross products
  Area = 0.5*b*h
  Length of cross product = 2*area of triangle
Matrix form

## Slide 15: Area Computation

## Slide 16: Barycentric Matrix Computation

## Slide 17: “Clipless” Homogeneous Rasterization
Extra edge equations for clip edges
  Compute clip plane at each vertex
  Only visible (w>near) pixels will be drawn
Adds computation,
  But avoids branching and extra triangles
  Good for hardware

## Slide 18: Barycentric Rasterization
For all x do
  For all y do
    Compute (a, b, g) for (x,y)
    If (a  [0,1] and b  [0,1] and g  [0,1] then
      c = ac0 + bc1 + gc2
      Draw pixel (x,y) with color c

## Slide 19: Barycentric Rasterization
xmin = floor(min(x0,x1,x2))
xmax = ceiling(max(x0,x1,x2))
ymin = floor(min(y0,y1,y2))
ymax = ceiling(max(y0,y1,y2))
for y = ymin to ymax do
  for x = xmin to xmax do
    a = f12(x,y)/f12(x0,y0)
    b = f20(x,y)/f20(x1,y1)
    g = f01(x,y)/f01(x2,y2)
    If (a  [0,1] and b  [0,1] and g  [0,1] then
      c = ac0 + bc1 + gc2
      Draw pixel (x,y) with color c

## Slide 20: Incremental Computation
a, b, and g are linear in x and y
What about a(x+1,y)?