CMSC 313 Spring 2011

Midterm Exam 2

Section 02

April 25, 2011

Name__________________________________Score __________ out of 70

UMBC Username ______________________________________________

Notes:

- Please write clearly.  Unreadable answers receive no credit.

- There are no intentional syntax errors in any code provided with this exam.  If you think you see an error that would affect your answer, please bring it to my attention.

- Use of a calculator is permitted.

Multiple Choice (2 points each)
Write the letter of the best choice in the appropriate box at the bottom of the page.

- By default, on Intel x86, the stack

  - is located at the bottom of memory.

  - grows down towards smaller addresses

  - grows up towards larger addresses

  - is located in the heap

- Which of the following registers stores the integer return value of functions in Intel x86?

(a) %eax

(b) %ecx

(c) %edx

(d) %esp

- The leave instruction is effectively the same as which of the following:

(a) mov %ebp, %esp

pop %ebp

(b) pop %eip

(c) mov %esp, %ebp

pop %esp

(d) ret

- In two’s compliment, what is the value of −TMin?

  - TMax

  - TMin

  - 0

  - −1

- Given the declaration short scores[ 3 ][ 4 ], the formula to  calculate the memory address of scores[x][y]  is
      (a) scores + 4 * x + y

(b) scores + 8 * x + 2 * y

(c) scores + 3 * x + y

(d) scores + 6 * x  + 2 * y

| 1. | 2. | 3. | 4. | 5. |
| --- | --- | --- | --- | --- |

- Which line of C code will perform the same operation as

leal 0x10 (%eax, ecx, 4), %eax?

(a) eax = 16 + eax + 4 * ecx

(b) eax = *(16 + eax + 4 * ecx)

(c) eax = 16 + *(eax + 4 * ecx)

(d)) eax = 16 + 4 * eax + ecx

- Which line of Intel x86 assembly will perform the same operation as

ecx = ((int *)eax + ecx)?

(a) movl (%eax, %ecx, 4),%ecx

(b) leal (%eax, %ecx, 4), %ecx

(c) leal (%eax, 4, %ecx), %ecx

(d) movl (%eax, 4, %ecx), %ecx

- The “target” of a buffer overflow attack is usually

(a) %esp

(b) %ebp

(c) The function return address

(d) The function arguments

- The two’s complement negation of the binary value 0100101101 is

(a) 1011011011

(b) 1011010010

(c) 1100101101

(d) 1011010011

- The return address for a function call is always found at

  - 0x8(%ebp)

  - 0x4(%ebp)

  - 0x8(%esp)

  - -0x4(%ebp)

| 6. | 7. | 8. | 9. | 10. |
| --- | --- | --- | --- | --- |

- For any signed integer, x, the value of    ~(x ^ x) + 1 is

  - 1

  - 0

  - TMax

  - dependent on the initial value of x

- Here is a small C program:

struct foo { int bar; int baz; };

int getBaz(struct foo *foo_ptr)

{

return foo_ptr->baz;

}

After compiling the code and disassembling getBaz, and adding a few 	comments, we get:

getBaz:

pushl %ebp 			# save old frame pointer

movl %esp,%ebp 		# set frame base pointer

movl 0x8(%ebp),%eax  	# move foo_ptr to %eax

–- Mystery  Instruction Goes Here -–

leave

ret

What is the "Mystery Instruction"?

(a) movl 0x4(%eax),%eax

(b) movl $baz(%eax),%eax

(c) leal 0x4(%eax),%eax

(d) movl 0xc(%ebp),%eax

| 11. | 12. |
| --- | --- |

14. (5 points) For this problem, assume the following:

• We are running code on a 6-bit machine using two’s complement 		arithmetic for signed integers.

• short integers are encoded using 3 bits.

• Sign extension is performed whenever a short is casted to an int

• Right shifts of signed integers are arithmetic.

Fill in the empty boxes in the table below. Note: You need not fill in entries marked with “--”.

The following definitions are used in the table:

int a = -23;

unsigned ua = a;

int x = -17;

short y = (short)x;

unsigned ux = x;

| Expression | Decimal | Binary |
| --- | --- | --- |
| -- |  | 100110 |
| x | -17 |  |
| y |  |  |
| ux |  |  |
| a >> 2 |  |  |
| ua >> 2 |  |  |

15. (10 points) Examine the disassembled code below (from gdb) for the function  int flush( int a, int b, int c) that implements a switch statement using integer cases, then answer the questions below.  Write your answers in the table below the questions.

Dump of assembler code for function flush:

0x08048384 <flush+0>:   push   %ebp

0x08048385 <flush+1>:   mov    %esp,%ebp

0x08048387 <flush+3>:   sub    $0x4,%esp

0x0804838a <flush+6>:   mov    0x8(%ebp),%eax

0x0804838d <flush+9>:   sub    $0xd2,%eax

0x08048392 <flush+14>:  mov    %eax,-0x4(%ebp)

0x08048395 <flush+17>:  cmpl   $0x9,-0x4(%ebp)

0x08048399 <flush+21>:  ja     0x80483c9 <flush+69>

0x0804839b <flush+23>:  mov    -0x4(%ebp),%edx

0x0804839e <flush+26>:  mov    0x80484f8(,%edx,4),%eax

0x080483a5 <flush+33>:  jmp    *%eax

0x080483a7 <flush+35>:  addl   $0x2,0xc(%ebp)

0x080483ab <flush+39>:  jmp    0x80483cd <flush+73>

0x080483ad <flush+41>:  mov    0xc(%ebp),%eax

0x080483b0 <flush+44>:  imul   0xc(%ebp),%eax

0x080483b4 <flush+48>:  mov    %eax,0xc(%ebp)

0x080483b7 <flush+51>:  jmp    0x80483cd <flush+73>

0x080483b9 <flush+53>:  mov    0x8(%ebp),%eax

0x080483bc <flush+56>:  sub    %eax,0xc(%ebp)

0x080483bf <flush+59>:  jmp    0x80483cd <flush+73>

0x080483c1 <flush+61>:  mov    0xc(%ebp),%eax

0x080483c4 <flush+64>:  add    %eax,0xc(%ebp)

0x080483c7 <flush+67>:  jmp    0x80483cd <flush+73>

0x080483c9 <flush+69>:  subl   $0x9,0xc(%ebp)

0x080483cd <flush+73>:  mov    0xc(%ebp),%eax

0x080483d0 <flush+76>:  add    0x8(%ebp),%eax

0x080483d3 <flush+79>:  leave

0x080483d4 <flush+80>:  ret

End of assembler dump.

(gdb) x/12w 0x80484f8

0x80484f8:      0x080483a7      0x080483ad      0x080483b9      0x080483c9

0x8048508:      0x080483c9      0x080483c9      0x080483b9      0x080483c9

0x8048518:      0x080483c9      0x080483c1      0x000a6425      0x00000000

Hint: 0xd2 = 210 in decimal

A. What is the highest case number in the switch?

B. Which two non-default cases share the same code?

C. Name one case that is missing from the switch.

D. What is the address of the default case?

E. What is the one line of C code in case 211?

| A | B | C | D | E |
| --- | --- | --- | --- | --- |

16. (10 points) Examine the disassembled code for the function fun1 that implements the while-loop in the lower box.  Fill in the blanks with the appropriate C code.  The length of each line is not necessarily indicative of the code.  The lines are just long for those with large handwriting.  Hint: 0x4d2 = 1234 decimal.

17. (7 points) Consider the structure definition below and then answer the questions below.

struct {

char a, b;

long *c;

char *d;

int e;

char f;

int g;

} foo;

a. (2 pts) How many bytes of padding will the compiler use inside of foo? ___________

b. (3 pts) Write a new definition of foo that minimizes the number of bytes of padding in the space  below.

c. (2 pts) How many bytes of padding does your foo definition require? _____________

Use the grids below to help visualize how a foo variable would be laid out in memory.

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+

18. ( 5 points) Examine the assembly language dump below.   Then complete the code for the function named sumElements2.

Dump of assembler code for function sumElements2.

0x080483a5 <sumElements2+0>:    push   %ebp

0x080483a6 <sumElements2+1>:    mov    %esp,%ebp

0x080483a8 <sumElements2+3>:    mov    0xc(%ebp),%eax

0x080483ab <sumElements2+6>:    shl    $0x2,%eax

0x080483ae <sumElements2+9>:    add    0x8(%ebp),%eax

0x080483b1 <sumElements2+12>:   add    $0x10,%eax

0x080483b4 <sumElements2+15>:   mov    (%eax),%ecx

0x080483b6 <sumElements2+17>:   mov    0x10(%ebp),%edx

0x080483b9 <sumElements2+20>:   mov    %edx,%eax

0x080483bb <sumElements2+22>:   shl    $0x2,%eax

0x080483be <sumElements2+25>:   add    %edx,%eax

0x080483c0 <sumElements2+27>:   shl    $0x2,%eax

0x080483c3 <sumElements2+30>:   add    0x8(%ebp),%eax

0x080483c6 <sumElements2+33>:   mov    (%eax),%eax

0x080483c8 <sumElements2+35>:   lea    (%ecx,%eax,1),%eax

0x080483cb <sumElements2+38>:   pop    %ebp

0x080483cc <sumElements2+39>:   ret    0x08048384

End of assembler dump.

int sumElements2(int a[],  int i, int j)

{

return ____________________________________;

}

19. (9 points) Match each of the functions on the left with the equivalent assembly language code block on the right. Write the letter of the assembly language code block in the box in the table below

Your answers go in this table

| Function | Assembly Code Block |
| --- | --- |
| fun1 |  |
| fun2 |  |
| fun3 |  |

# Text boxes

int fun1( int x, int y)

{

return x * 12 - y * 2;

}

int fun2 (int x, int y)

{

return (x + y) * 14;

}

int fun3( int x, int y )

{

return y * 63 + x;

}

Code Block A:

d0:   55          push   %ebp

d1:   89 e5       mov    %esp,%ebp

d3:   8b 55 0c    mov    0xc(%ebp),%edx

d6:   89 d0       mov    %edx,%eax

d8:   c1 e0 06    shl    $0x6,%eax

db:   29 d0       sub    %edx,%eax

dd:   8b 55 08    mov    0x8(%ebp),%edx

e0:   5d          pop    %ebp

e1:   01 d0       add    %edx,%eax

e3:   c3          ret

Code Block B:

f0:   55          push   %ebp

f1:   89 e5       mov    %esp,%ebp

f3:   8b 45 08    mov    0x8(%ebp),%eax

f6:   8b 55 0c    mov    0xc(%ebp),%edx

f9:   5d          pop    %ebp

fa:   8d 04 40    lea    (%eax,%eax,2),%eax

fd:   c1 e0 02    shl    $0x2,%eax

100:   01 d2       add    %edx,%edx

102:   29 d0       sub    %edx,%eax

104:   c3          ret

Code Block C:

110:   55           push   %ebp

111:   89 e5        mov    %esp,%ebp

113:   8b 45 0c     mov    0xc(%ebp),%eax

116:   8b 4d 08     mov    0x8(%ebp),%ecx

119:   5d           pop    %ebp

11a:   01 c8        add    %ecx,%eax

11c:   8d 14 00     lea   (%eax,%eax,1),%edx

11f:   c1 e0 04     shl    $0x4,%eax

122:   29 d0        sub    %edx,%eax

124:   c3           ret

Code Block D:

130:   55           push   %ebp

131:   89 e5        mov    %esp,%ebp

133:   8b 4d 0c     mov    0xc(%ebp),%ecx

136:   8b 45 08     mov    0x8(%ebp),%eax

139:   5d           pop    %ebp

13a:   89 ca        mov    %ecx,%edx

13c:   c1 e2 04     shl    $0x4,%edx

13f:   c1 e0 06     shl    $0x6,%eax

142:   29 ca        sub    %ecx,%edx

144:   29 d0        sub    %edx,%eax

146:   c3           ret

Dump of assembler code for function fun1:

0x08048384 <fun2+0>:    pushl   %ebp

0x08048385 <fun2+1>:    movl    %esp,%ebp

0x08048387 <fun2+3>:    subl    $0x10,%esp

0x0804838a <fun2+6>:    movl    $0x4d2,-0x4(%ebp)

0x08048391 <fun2+13>:   jmp     0x804839a <fun2+22>

0x08048393 <fun2+15>:   sarl    $0x2,-0x4(%ebp)

0x08048397 <fun2+19>:   incl    0x10(%ebp)

0x0804839a <fun2+22>:   mov     0xc(%ebp),%eax

0x0804839d <fun2+25>:   addl    $0x5,%eax

0x080483a0 <fun2+28>:   cmp     0x10(%ebp),%eax

0x080483a3 <fun2+31>:   jg      0x8048393 <fun2+15>

0x080483a5 <fun2+33>:   movl    0x8(%ebp),%eax

0x080483a8 <fun2+36>:   addl    -0x4(%ebp),%eax

0x080483ab <fun2+39>:   leave

0x080483ac <fun2+40>:   ret

End of assembler dump.

int fun2( int a, int b, int c )

{

int x = __________;

while (_______________________ )

{

______________________ ;

_______________________;

}

return _____________________;

}