I/O Systems
Dr. Richard Carback
<carback1@umbc.edu>
http://www.csee.umbc.edu/courses/undergraduate/421/Spring12/02/
Slides based on Operating Systems Concepts, 8th Edition

---
Overview
- I/O Hardware
- Application I/O Interface
- Kernel I/O Subsystem
- Transforming I/O Requests to Hardware Operations
- STREAMS
- Performance
[Speaker Notes: Explore the structure of an operating system’s I/O subsystem Discuss the principles of I/O hardware and its complexity Provide details of the performance aspects of I/O hardware and software]

---
[Speaker Notes: I/O management is a major component of operating system design and operation Important aspect of computer operation I/O devices vary greatly Various methods to control them Performance management New types of devices frequent Ports, busses, device controllers connect to various devices Device drivers encapsulate device details Present uniform device-access interface to I/O subsystem]

---
https://en.wikipedia.org/wiki/File:Motherboard_diagram.svg
[Speaker Notes: Incredible variety of I/O devices Storage Transmission Human-interface Common concepts – signals from I/O devices interface with computer Port – connection point for device Bus - daisy chain or shared direct access Controller (host adapter ) – electronics that operate port, bus, device Sometimes integrated Sometimes separate circuit board (host adapter) Contains processor, microcode, private memory, bus controller, etc Some talk to per-device controller with bus controller, microcode, memory, etc]

---
https://en.wikipedia.org/wiki/File:Schema_chipsatz.png
[Speaker Notes: I/O instructions control devices Devices usually have registers where device driver places commands, addresses, and data to write, or read data from registers after command execution Data-in register, data-out register, status register, control register Typically 1-4 bytes, or FIFO buffer Devices have addresses, used by Direct I/O instructions Memory-mapped I/O Device data and command registers mapped to processor address space Especially for large address spaces (graphics)]

---
https://en.wikipedia.org/wiki/File:IBM_T42_Motherboard_IMG_2591a.jpg

---
Polling
Polling
For each byte of I/O
  - Read busy bit from status register until 0
  - Host sets read or write bit and if write copies data into data-out register
  - Host sets command-ready bit
  - Controller sets busy bit, executes transfer
  - Controller clears busy bit, error bit, command-ready bit when transfer done
Step 1 is busy-wait cycle to wait for I/O from device
  - Reasonable if device is fast
  - But inefficient if device slow
  - CPU switches to other tasks?
    - But if miss a cycle data overwritten / lost

---
Interrupts
Interrupts
- Polling can happen in 3 instruction cycles
  - Read status, logical-and to extract status bit, branch if not zero
  - How to be more efficient if non-zero infrequently?
- CPU Interrupt-request line triggered by I/O device
  - Checked by processor after each instruction
- Interrupt handler receives interrupts
  - Maskable to ignore or delay some interrupts
- Interrupt vector to dispatch interrupt to correct handler
  - Context switch at start and end
  - Based on priority
  - Some nonmaskable
  - Interrupt chaining if more than one device at same interrupt number

---
[Speaker Notes: Interrupt mechanism also used for exceptions Terminate process, crash system due to hardware error Page fault executes when memory access error System call executes via trap to trigger kernel to execute request Multi-CPU systems can process interrupts concurrently If operating system designed to handle it Used for time-sensitive processing, frequent, must be fast]

---
Block & Character Devices
- Block devices include disk drives
  - Commands include read, write, seek
  - Raw I/O , direct I/O , or file-system access
  - Memory-mapped file access possible
  - File mapped to virtual memory and clusters brought via demand paging
  - DMA
- Character devices include keyboards, mice, serial ports
  - Commands include get(), put()
  - Libraries layered on top allow line editing

---
Network Cards
- Varying enough from block and character to have own interface
- Unix and Windows NT/9x /2000 include socket interface
  - Separates network protocol from network operation
  - Includes select() functionality
- Approaches vary widely (pipes, FIFOs, streams, queues, mailboxes)

---
Clocks/Timers
- Provide current time, elapsed time, timer
- Normal resolution about 1/60 second
- Some systems provide higher-resolution timers
- Programmable interval timer used for timings, periodic interrupts
- ioctl() (on UNIX) covers odd aspects of I/O such as clocks and timers

---
[Speaker Notes: Blocking - process suspended until I/O completed Easy to use and understand Insufficient for some needs Nonblocking - I/O call returns as much as available User interface, data copy (buffered I/O) Implemented via multi-threading Returns quickly with count of bytes read or written select() to find if data ready then read() or write() to transfer Asynchronous - process runs while I/O executes Difficult to use I/O subsystem signals process when I/O completed]

---
Kernel IO Subsystems
- Scheduling
  - Some I/O request ordering via per-device queue
  - Some OSs try fairness
  - Some implement Quality Of Service (i.e. IPQOS)
- Buffering - store data in memory while transferring between devices
  - To cope with device speed mismatch
  - To cope with device transfer size mismatch
  - To maintain “copy semantics”
  - Double buffering – two copies of the data
    - Kernel and user
    - Varying sizes
    - Full / being processed and not-full / being used
    - Copy-on-write can be used for efficiency in some cases

---
Device Transfer Rates

---
Kernel I/O Subsystem
- Caching - faster device holding copy of data
  - Always just a copy
  - Key to performance
  - Sometimes combined with buffering
- Spooling - hold output for a device
  - If device can serve only one request at a time
  - i.e., Printing
- Device reservation - provides exclusive access to a device
  - System calls for allocation and de-allocation
  - Watch out for deadlock

---
Error Handling
Error Handling
- OS can recover from disk read, device unavailable, transient write failures
  - Retry a read or write, for example
  - Some systems more advanced – Solaris FMA, AIX
    - Track error frequencies, stop using device with increasing frequency of retry-able errors
- Most return an error number or code when I/O request fails
- System error logs hold problem reports

---
I/O Protection
I/O Protection
- User process may accidentally or purposefully attempt to disrupt normal operation via illegal I/O instructions
  - All I/O instructions defined to be privileged
  - I/O must be performed via system calls
    - Memory-mapped and I/O port memory locations must be protected too

---
[Speaker Notes: Kernel keeps state info for I/O components, including open file tables, network connections, character device state Many, many complex data structures to track buffers, memory allocation, “dirty” blocks Some use object-oriented methods and message passing to implement I/O Windows uses message passing Message with I/O information passed from user mode into kernel Message modified as it flows through to device driver and back to process Pros / cons?]

---
[Speaker Notes: Consider reading a file from disk for a process: Determine device holding file Translate name to device representation Physically read data from disk into buffer Make data available to requesting process Return control to process]

---
[Speaker Notes: STREAM – a full-duplex communication channel between a user-level process and a device in Unix System V and beyond A STREAM consists of: - STREAM head interfaces with the user process - driver end interfaces with the device - zero or more STREAM modules between them Each module contains a read queue and a write queue Message passing is used to communicate between queues Flow control option to indicate available or busy Asynchronous internally, synchronous where user process communicates with stream head]

---
Performance
Performance
- I/O a major factor in system performance:
  - Demands CPU to execute device driver, kernel I/O code
  - Context switches due to interrupts
  - Data copying
  - Network traffic especially stressful

---
Intercomputer Communications

---
Improving Performance
Improving Performance
- Reduce number of context switches
- Reduce data copying
- Reduce interrupts by using large transfers, smart controllers, polling
- Use DMA
- Use smarter hardware devices
- Balance CPU, memory, bus, and I/O performance for highest throughput
- Move user-mode processes / daemons to kernel threads

---
Device-Functionality Progression

---
Questions?