## Slide 1: CMSC 611: Advanced Computer Architecture
Cache
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Memory Hierarchy
Control
Datapath
Secondary
Storage
(Disk)
Processor
Registers
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
On-Chip
Cache
Fastest
Slowest
Smallest
Biggest
Highest
Lowest
Speed:
Size:
Cost:
Compiler
Hardware
Operating System
Temporal Locality (Locality in Time):
   Keep most recently accessed data items closer to the processor
Spatial Locality (Locality in Space):
   Move blocks consists of contiguous words to the faster levels

## Slide 3: Memory Hierarchy Terminology
Slower Level
Memory
Faster Level
Memory
To Processor
From Processor
Block X
Block Y
Hit: data appears in some block in the faster level (example: Block X)
  Hit Rate: the fraction of memory access found in the faster level
  Hit Time: Time to access the faster level which consists of
    Memory access time + Time to determine hit/miss
Miss: data needs to be retrieve from a block in the slower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level + Time to deliver the block the processor
Hit Time << Miss Penalty

## Slide 4: Memory Hierarchy Design Issues
Block identification
  How is a block found if it is in the upper (faster) level?
    Tag/Block
Block placement
  Where can a block be placed in the upper (faster) level?
    Fully Associative, Set Associative, Direct Mapped
Block replacement
  Which block should be replaced on a miss?
    Random, LRU
Write strategy
  What happens on a write?
    Write Back or Write Through (with Write Buffer)

## Slide 5: The Basics of Cache
Requesting Xn generates a miss and the word Xn will be brought from main memory to cache
Issues:
How do we know that a data item is in cache?
If so, How to find it?
Cache: level of hierarchy closest to processor
Caches first appeared in research machines in early 1960s
In every general-purpose computer produced today

## Slide 6: Direct-Mapped Cache
Cache block address = (Block address) modulo (Number of cache blocks)
Memory words can be mapped only to one cache block
Cache Data
Valid Bit
Byte 0
Byte 1
Byte 3
Cache Tag
Byte 2
Worst case is to keep replacing a block followed by a miss for it: Ping Pong Effect
To reduces misses:
  make the cache size bigger
  multiple entries for the same Cache Index

## Slide 7: Accessing Cache
Size depends on:
  # cache blocks
  Tag size
  Block size
Example:
  For 32-bit address 1024 4-byte blocks
  Data size
  = 4*1024 B = 4096 B
  Physical size
  = (data+tag+valid)*lines
  = (32+20+1)*1024 bits
  = 53*1024 bits = 6784 B

## Slide 8: Cache with Multi-Word/Block
Takes advantage of spatial locality to improve performance
Cache block address = (Block address) modulo (Number of cache blocks)
Block address = (byte address) / (bytes per block)

## Slide 9: Measuring Cache Performance
Compute Average Access Time
Miss penalty for L1 is the average access time for L2
Together, computes Average Memory Access Time (AMAT)

## Slide 10: Determining Block Size
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks:
compromises
temporal locality
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
Block Size
Larger block size take advantage of spatial locality BUT:
  Larger block size means larger miss penalty:
    Takes longer time to fill up the block
  If block size is too big relative to cache size, miss rate will go up
    Too few cache blocks
Typical size today = 64 bytes (16 32-bit words)
Average Access Time = Hit Time + Miss Penalty * Miss Rate

## Slide 11: Block Placement
Cache utilization
Hardware Complexity
Set number = (Block number) modulo (Number of sets in the cache)
Increased flexibility of block placement reduces probability of cache misses

## Slide 12: N-way Set Associative Cache
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Index
Mux
0
1
Sel1
Sel0
Cache Block
Compare
Adr Tag
Compare
OR
Hit
N entries for each Cache Index
Example: Two-way set associative cache
  Cache Index selects a “set” from the cache
  The two tags in the set are compared in parallel
  Data is selected based on the tag result

## Slide 13: Locating a Block in Associative Cache
Tag size increases with higher level of associativity

## Slide 14: Fully Associative Cache
:
Cache Data
Byte 0
0
4
31
:
Cache Tag (27 bits long)
Valid Bit
:
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Cache Tag
Byte Select
Ex: 0x01
X
X
X
X
X
Forget about the Cache Index
Compare the Cache Tags of all cache entries in parallel
Example: Block Size = 32 Byte blocks, we need N 27-bit comparators
By definition: Conflict Miss = 0 for a fully associative cache
Notes: Direct mapped = simple / fully associative = complex
Like N-way set associative with N = # cache entries
i.e. no cache index bits in address.
Very hardware intensive: usually, fully associative cache is limited to 64 or less entries.
Never conflict, but can have Capacity Miss (on 65th item in 64-element cache)

## Slide 15: Handling Cache Misses
Read misses bring blocks from memory
Write access requires careful maintenance of consistency between cache and main memory
Two write strategies:
  Write through: write to both cache and memory
    Read misses cannot result in writes
    No allocation of a cache block is needed
    Always combined with write buffers so that don’t wait for slow memory
  Write back: write cache only; write to memory when cache block is replaced
    Is block clean or dirty?
    No writes to slow memory for repeated write accesses
    Requires allocation of a cache block

## Slide 16: Write Through via Buffering
Processor
Cache
Write Buffer
DRAM
Processor writes data into the cache and the write buffer
Memory controller writes contents of the buffer to memory
Increased write frequency can cause saturation of write buffer
If CPU cycle time too fast and/or too many store instructions in a row:
  Store buffer will overflow no matter how big you make it
  The CPU Cycle Time get closer to DRAM Write Cycle Time
Write buffer saturation can be handled by installing a second level (L2) cache
Processor
Cache
Write Buffer
DRAM
L2
Cache

## Slide 17: Block Replacement Strategy
Empirical results indicates less significance of replacement strategy with
increased cache sizes
Straight forward for Direct Mapped since every block has only one location
Set Associative or Fully Associative:
  Random: pick any block
  LRU (Least Recently Used)
    requires tracking block reference
    for two-way set associative cache, reference bit attached to every block
    more complex hardware is needed for higher level of cache associativity

## Slide 18: Measuring Cache Performance
For write-through scheme:
Hard to control, assume enough buffer size
To enhance cache performance, one can:
  Reduce the miss rate (e.g. diminishing blocks collisions)
  Reduce the miss penalty (e.g. adding multi-level caching)
  Enhance hit access time (e.g. simple and small cache)