## Slide 1: CMSC 611: Advanced Computer Architecture
Instruction Level Parallelism
Some material adapted from Mohamed Younis, UMBC CMSC 611 Spr 2003 course slides
Some material adapted from Hennessy & Patterson / © 2003 Elsevier Science

## Slide 2: Floating-Point Pipeline
Impractical for FP ops to complete in one clock
  (complex logic and/or very long clock cycle)
More complex hazards
  Structural
  Data

## Slide 3: Multi-cycle FP Pipeline
Non-pipelined DIV operation stalling the whole pipeline for 24 cycles
4-stage pipelined FP addition
Integer ALU
7-stage pipelined FP multiply
Example: blue indicate where data is needed and red when result is available

## Slide 4: Multi-cycle FP: EX Phase
Latency: cycles between instruction that produces result and instruction that uses it
  Since most operations consume their operands at the beginning of the EX stage, latency is usually number of the stages of the EX an instruction uses
Long latency increases the frequency of RAW hazards
Initiation interval / Repeat interval: cycles between issuing two operations of a given type

## Slide 5: FP Pipeline Challenges
Example of RAW hazard caused by the long latency
Non-pipelined divide causes structural hazards
Number of register writes required in a cycle can be larger than 1
WAW hazards are possible
  Instructions no longer reach WB in order
WAR hazards are NOT possible
  Register reads are still taking place during the ID stage
Instructions can complete out of order
  Complicates exceptions
Longer latency makes RAW stalls more frequent

## Slide 6: Structural Hazard
At cycle 10, MULTD, ADDD and LD instructions all in MEM
At cycle 11, MULTD, ADDD and LD instructions all in WB
  Additional write ports are not cost effective since they are rarely used
Instead
  Detect at ID and stall
  Detect at MEM or WB and stall

## Slide 7: WAW Data Hazards
WAW hazards can be corrected by either:
  Stalling the latter instruction at MEM until it is safe
  Preventing the first instruction from overwriting the register
Correcting at cycle 11 OK unless intervening RAW/use of F2
WAW hazards can be detected at the ID stage
  Convert 1st instruction to no-op
WAW hazards are generally very rare, designers usually go with the simplest solution

## Slide 8: Detecting Hazards
Hazards among FP instructions & and combined FP and integer instructions
Separate int & fp register files limits latter to FP load and store instructions
Assuming all checks are to be performed in the ID phase:
  Check for structural hazards:
    Wait if the functional unit is busy (Divides in our case)
    Make sure the register write port is available when needed
  Check for a RAW data hazard
    Requires knowledge of latency and initiation interval to decide when to forward and when to stall
  Check for a WAW data hazard
    Write completion has to be estimated at the ID stage to check with other instructions in the pipeline
Data hazard detection and forwarding logic from values stored between the stages

## Slide 9: Stalls/Instruction, FP Pipeline

## Slide 10: Instruction Level Parallelism (ILP)
Overlap the execution of unrelated instructions
Both instruction pipelining and ILP enhance instruction throughput not the execution time of the individual instruction
Potential of IPL within a basic block is very limited
  In gcc 17% of instructions are control transfer meaning on average 5 instructions per branch

## Slide 11: Loops: Simple & Common
for (i=1; i<=1000; i=i+1) x[i] = x[i] + y[i];
Techniques like loop unrolling convert loop-level parallelism into instruction-level parallelism
  statically by the compiler
  dynamically by hardware
Loop-level parallelism can also be exploited using vector processing
IPL feasibility is mainly hindered by data and control dependence among the basic blocks
Level of parallelism is limited by instruction latencies

## Slide 12: Major Assumptions
Basic MIPS integer pipeline
Branches with one delay cycle
Functional units are fully pipelined or replicated (as many times as the pipeline depth)
  An operation of any type can be issued on every clock cycle and there are no structural hazard

## Slide 13: Motivating Example
for(i=1000; i!=0; i=i-1)
x[i] = x[i] + s;
Standard Pipeline execution
Sophisticated compiler optimization reduced execution time from 10 cycles to only 6 cycles
Loop: LD F0,x(R1) ;F0=x[i]
ADDD F4,F0,F2 ;add F2(=s)
SD x(R1),F4 ;store result
SUBI R1,R1,8 ;i=i-1
BNEZ R1,Loop ;loop to 0
Loop: LD F0,x(R1)
stall
ADDD F4,F0,F2
stall
stall
SD x(R1),F4
SUBI R1,R1,8
stall
BNEZ R1,Loop
stall
Loop: LD F0,x(R1)
SUBI R1,R1,8
ADDD F4,F0,F2
stall ;F4
BNEZ R1,Loop
SD x+8(R1),F4
Smart compiler

## Slide 14: Loop Unrolling
Loop: LD F0,x(R1)
ADDD F4,F0,F2
SD x(R1),F4
LD F6,x-8(R1) ;drop SUBI/BNEZ
ADDD F8,F6,F2
SD x-8(R1),F8
LD F10,x-16(R1) ;drop again
ADDD F12,F10,F2
SD x-16(R1),F12
LD F14,x-24(R1) ;drop again
ADDD F16,F14,F2
SD x-24(R1),F16
SUBI R1,R1,32 ;alter to 4*8
BNEZ R1,LOOP
Loop: LD F0,x(R1) ADDD F4,F0,F2 SD x(R1),F4 SUBI R1,R1,8 BNEZ R1,Loop
Replicate loop body 4 times, will need cleanup
phase if loop iteration is not a multiple of 4
6 cycles, but only 3 are loop body
Loop unrolling limits overhead at the expense of a larger code
  Eliminates branch delays
  Enable effective scheduling
Use of different registers needed to limit data hazard

## Slide 15: Scheduling Unrolled Loops
Cycle Instruction
1 Loop: LD F0,x(R1)
3 ADDD F4,F0,F2
6 SD x(R1),F4
7 LD F6,x-8(R1)
9 ADDD F8,F6,F2
12 SD x-8(R1),F8
13 LD F10,x-16(R1)
15 ADDD F12,F10,F2
18 SD x-16(R1),F12
19 LD F14,x-24(R1)
21 ADDD F16,F14,F2
24 SD x-24(R1),F16
25 SUBI R1,R1,#32
27 BNEZ R1,LOOP
28 NOOP
Cycle Instruction
1 Loop: LD F0,x(R1)
2 LD F6,x-8(R1)
3 LD F10,x-16(R1)
4 LD F14,x-24(R1)
5 ADDD F4,F0,F2
6 ADDD F8,F6,F2
7 ADDD F12,F10,F2
8 ADDD F16,F14,F2
9 SD x(R1),F4
10 SD x-8(R1),F8
11 SUBI R1,R1,#32
12 SD x+16(R1),F12
13 BNEZ R1,LOOP
14 SD x+8(R1),F1
Loop unrolling exposes more computation that can be scheduled to minimize the pipeline stalls
Understanding dependence among instructions is the key for for detecting and performing the transformation